## Slide 1: Distributed Network
Weichun Xu
Advisor: Fareena Saqib

## Slide 2: Content
Introduction
Design Structure and Command Format
Debug Structure
Verification Environment and Test List
Simulation Result and Code Coverage
Reference

## Slide 3: Introduction
Distributed Network
Distributed computing network system
Part of distributed computing architecture
Deliver the data to remote computers for processing
2 kinds of distributed computing system
Distributed computing system models
Multiprocessing that takes place on one computer
Run programs in parallel on multiple computers
Traditional client/server computing model
Cloud computing model

## Slide 4: Introduction
Current research focus on using CPUs or GPUs to process data in parallel, e.g.:
  Using tens of thousands of CPU cores to realize large scale distributed deep networks
In the presentation, we will focus on using FPGA parallel computing

## Slide 5: Design Structure
rx
uart2fifo_ctrl
fifo0
fifo1
fifo2
fifo3
fifo0
fifo1
fifo2
fifo3
spi_m0
spi_m1
spi_m2
spi_m3
spi_s0
spi_s1
spi_s2
spi_s3
fifo0
fifo1
fifo2
fifo3
spi_s0
spi_s1
spi_s2
spi_s3
spi_m0
spi_m1
spi_m2
spi_m3
fifo0
fifo1
fifo2
fifo3
rx
uart2fifo_ctrl
tx_fsm_start
register
dn_host
dn_device0~3

## Slide 6: Command Format
0 | 0 | 1 | x | 0 | addr[2] | addr[1] | addr[0]
data[7] | data[6] | data[5] | data[4] | data[3] | data[2] | data[1] | data[0]
0 | 1 | 0 | x | 0 | addr[2] | addr[1] | addr[0]
  Read Register
  Write Register
cmd[2] | cmd[1] | cmd[0] | broadcast/unicast | fifo/register | addr[2] | addr[1] | addr[0]
  Command Byte Format:
  cmd[2:0]: 0x1 – write; 0x2 - read
  broadcast/unicast: 1 – broadcast; 0 – unicast #broadcast is useless for writing/reading register
  fifo/register: 1 – fifo; 0 – register
  addr[2:0]: register address; range in [0:7] #addr is useless for writing/reading fifo

## Slide 7: Command Format
0 | 0 | 1 | 0 | 1 | x | x | x
length[7] | length[6] | length[5] | length[4] | length[3] | length[2] | length[1] | length[0]
data[0][7] | data[0][6] | data[0][5] | data[0][4] | data[0][3] | data[0][2] | data[0][1] | data[0][0]
…… |  |  |  |  |  |  | 
data[length-1][7] | data[length-1][6] | data[length-1][5] | data[length-1][4] | data[length-1][3] | data[length-1][2] | data[length-1][1] | data[length-1][0]
  Write Fifo
0 | 0 | 1 | 1 | 1 | x | x | x
length[7] | length[6] | length[5] | length[4] | length[3] | length[2] | length[1] | length[0]
data[0][7] | data[0][6] | data[0][5] | data[0][4] | data[0][3] | data[0][2] | data[0][1] | data[0][0]
…… |  |  |  |  |  |  | 
data[length-1][7] | data[length-1][6] | data[length-1][5] | data[length-1][4] | data[length-1][3] | data[length-1][2] | data[length-1][1] | data[length-1][0]
    Broadcast Mode
0 | 1 | 0 | x | 1 | x | x | x
  Read Fifo
    Unicast Mode

## Slide 8: Debug Structure
rx
uart2fifo_ctrl
fifo0
fifo1
fifo2
fifo3
fifo0
fifo1
fifo2
fifo3
spi_m0
spi_m1
spi_m2
spi_m3
spi_s0
spi_s1
spi_s2
spi_s3
fifo0
fifo1
fifo2
fifo3
spi_s0
spi_s1
spi_s2
spi_s3
spi_m0
spi_m1
spi_m2
spi_m3
fifo0
fifo1
fifo2
fifo3
rx
uart2fifo_ctrl
rx_tx_loopback_en
uart2spi_fifo_loopback_en
spi_loopback_en
spi_fifo_loopback_en

## Slide 9: Debug Structure
dn_host_debug_en
dn_device_debug_en
ctrl
0
1
2
3
0
1
2
0
0
1
2
ctrl register
ctrl[2]
ctrl[1]
ctrl[0]
ctrl[3]
Pin
virtual_env
dn_host
dn_device
rx_tx_loopback_en
uart2spi_fifo_loopback_en
spi_loopback_en
spi_fifo_loopback_en
ctrl
ctrl
0
0
0
0
0
0

## Slide 10: Verification Environment
uart sequencer
uart driver
DUT
uart scoreboard (include RM)
uart monitor
uart transaction
tx
uart transaction
uart transaction
rx

## Slide 11: Test List
Test Name | Description
uart_multiple_write_reg_test | Check register path
uart_multiple_write_fifo_unicast_test | Check data path, verify unicast mode and write one byte
uart_multiple_write_fifo_burst_unicast_test | Check data path, verify unicast mode and write multiple bytes
uart_multiple_write_fifo_broadcast_test | Check data path, verify broadcast mode and write one byte
uart_multiple_write_fifo_burst_broadcast_test | Check data path, verify broadcast mode and write multiple bytes
uart_multiple_write_fifo_randcast_test | Check data path, write one byte, random unicast and broadcast
uart_multiple_write_fifo_burst_randcast_test | Check data path, write multiple bytes, random unicast and broadcast
uart_rx_tx_loopback_test | Loopback uart tx to uart tx
uart_hard_uart2spi_fifo_loopback_test | Use pin to enable debug mode and enable SPI fifo loopback in dn_host
uart_soft_uart2spi_fifo_loopback_test | Use register to enable debug mode and enable SPI fifo loopback in dn_host
uart_hard_spi_loopback_test | Use pin to enable debug mode and enable SPI loopback in dn_host
uart_soft_spi_loopback_test | Use register to enable debug mode and enable SPI loopback in dn_host

## Slide 12: Simulation Result
Rx to Tx loopback

## Slide 13: Simulation Result
Write/Read Register

## Slide 14: Simulation Result
Write/Read one byte with Unicast mode

## Slide 15: Simulation Result
Write/Read one byte with Broadcast mode

## Slide 16: Simulation Result
Write/Read multiple bytes with Unicast mode

## Slide 17: Simulation Result
Write/Read multiple bytes with Broadcast mode

## Slide 18: Code Coverage

## Slide 19: Future Work
Design
Use High Speed Interface (SATA, PCIE, etc.)
Parity check or CRC check between UART transmission
Handshake between dn_host and dn_device for quality assurance
Control the start of SPI Master in dn_host
Verification
Enhance code coverage
Enhance the scoreboard to make it more flexible
Add assertion on loopback path
Add Functional coverage

## Slide 20: Reference
Jeffrey Dean, Greg S. Corrado, Rajat Monga, Kai Chen, Matthieu Devin, Quoc V. Le, Mark Z. Mao, Marc’Aurelio Ranzato, Andrew Senior, Paul Tucker, Ke Yang and Andrew Y. Ng: Large Scale Distributed Deep Networks
Erik Nygren, Ramesh K. Sitaraman and Jennifer Sun: The Akamai Network: A Platform for High-Performance Internet Applications
Chee Shin Yeo, Rajkumar Buyya, Hossein Pourreza, Rasit Eskicioglu, Peter Graham and Frank Sommers: Cluster Computing: High-Performance, High-Availability, and High-Throughput Processing on a Network of Computers
David P. Anderson, Eric Korpela and Rom Walton: High-Performance Task Distribution for Volunteer Computing

## Slide 21: Q&A
Thank You